MARS EXPLORATION ROVER:

OVERVIEW OF CURRENT ELLIPSES OF

POTENTIAL LANDING SITES

M. Golombek and T. Parker

Mars Exploration Rover

Landing Site Workshop II

October 17, 2001

Pasadena, CA

# LANDING SITES ELLIPSE CHANGES

## SITE ELLIPSES

### Doppler and Range Tracking and 5 TCMs

220 to 70 km by 30 km for MER A ROTO Sites

340 to 140 km by 30 km for MER B ROTO Sites

## SMALL ELLIPSES

DeltaDOR and 5 TCMs Estimate w/o Margin

92 to 43 km by 8-11 km for MER A ROTO Sites

158 to 68 km by 9-11 km for MER B ROTO Sites

## PRESENT ELLIPSES

DeltaDOR and 5 TCMs Analysis with Margin

132 to 96 km by 16-19 km for MER A ROTO Sites

140 to 105 km by 16-20 km for MER B ROTO Sites

## ELLIPSE GROWTH TO S FOR MER A

### Gale, Boedickker, EP69A, Central & NE VM Outflow Ellipses No Longer Fit

# LANDING SITES WITH SMALL ELLIPSES

## DeltaDOR PLUS 5 TCMs

Small (0.5) Ellipses Possible-Smaller than considered previously for MER

Are there High Priority Sites of Smaller Ellipse Size?

## EVALUATED ALL MS ’01 LANDING SITES

Within MER Elevation and Latitude Band

##### LOOKED AT AREAS WITH SIGNIFICANT MOC COVERGAE

Within MER Elevation and Latitude Band

## SITES HAD TO MEET CRITERIA

All Engineering Criteria – elevation, smooth flat

thermal inertia, albedo, rock abundance

### As Scientifically Compelling as Existing ROTO and Nadir Sites

## NINE POSSIBLE SITES IDENTIFIED

3 Eliminated by Slightly Larger Ellipse

Isidis, Elysium Flow Site, 3 Highland Sites in Terra Meridiani

# REQUIREMENTS ON BACKUP ELLIPSES

## RETAIN FEW BACKUP ELLIPSES

Just in Case Some of Prime Sites Become Problematic

## INCLUDE IN MOC IMAGE QUEUE FOR NADIR IMAGES

If within 5° of End of ROTO Ellipse – unlikely to get images

## IF HEMATITE REMAINS A FAVORITE

No Backup Within 37° (i.e., No Closer than Valles Marineris)

Presentation Includes Images of all Landing Sites

Being Considered at Workshop

Sent In Separate Files