# SUMMARY OF LANDING SITE SAFETY EVALUATIONS

M. P. Golombek

F. S. Anderson

N. Bridges

JPL

M. Kennedy

Caltech

Mars Exploration Rover

Landing Site Selection Workshop II

October 17-18, 2001

Pasadena, CA

##### TOP 6 LANDING SITES

THERMOPHYSICAL PROPERTIES

##### IRTM and TES Albedo Data Set Courtesy P. Christensen

TES Thermal Inertia from Mellon et al. [2000]

Landing Site

Elysium Planitia

EP49B

Gale Crater

EP82A

Gusev Crater

EP55A South

Hematite (Meridiani)

TM9A

TM10A

TM19B

TM20B

TM21B

Isidis Planitia

IP84A

IP85A

IP96B

IP98B

Melas Chasma

VM53A

VM53"B"

Vallis Marineris outflow

VM41A

TES Bulk TI mean

194.74

323.24

302.54

263.34

254.19

263.70

257.56

243.43

487.54

465.90

507.20

487.60

308.32

307.95

397.03

TES Albedo mean

0.275

0.215

0.230

0.157

0.160

0.154

0.153

0.131

0.227

0.221

0.226

0.215

0.168

0.168

0.138

IRTM FC TI mean

207.21

240.35

247.67

298.17

308.62

298.17

307.23

290.93

392.92

368.89

378.29

352.51

253.31

253.31

298.17

IRTM Rocks mean

9.86

15.00

5.75

6.33

6.33

6.33

5.50

6.40

15.25

16.00

17.83

16.33

11.60

11.60

14.67

# COARSE INTERPRETATION OF LANDING SITES

Based on TES Thermal Inertia and Albedo & IRTM Fine Component Thermal Inertia and Rock Abundance and Comparisons to VL1, 2 and MPF Sites

GALE, EP82A

Thermal Inertia, Albedo, Rock Abundance Similar to VL and MPF Sites

Probably Like 3 Landing Sites – Rocky but less Dust

Gusev, EP55A

Similar to Gale but Fewer Rocks

Low to Moderate Rocks and Moderately Dusty

Hematite Sites

Moderate Thermal Inertia and Fine Component Thermal Inertia, Very Low Albedo, Few Rocks

Completely Unlike the 3 Landing Sites, Probably Little Dust

Isidis Sites

High Thermal Inertia and High Fine Component Thermal Inertia, Moderate Albedo, High Rock Abundance, [High Red/Blue Ratio, (to N)]

Rocky Sites with Possibly Weathered Crusty Surface

Melas Chasma Sites

Moderate Thermal Inertia (Bulk and Fine Component), Moderate Rocks, Low Albedo

Moderately Rocky Sites with Little Dust, Unlike 3 Landing Sites

EOS Chasma

High Bulk Thermal Inertia and Moderate Fine Component Thermal Inertia, Rocky, Low Albedo

Rocky and Crusty Surface with Little Dust

TABLE OF THERMOPHYSICAL PROPERTIES OF NADIR LANDING SITES

| Landing Site | TES Bulk TI | TES Albedo | IRTM FC TI | IRTM Rocks |
| --- | --- | --- | --- | --- |
| Hematite |  |  |  |  |
| TM22B | 290 | 0.147 | 303 | 7 |
| TM23B | 244 | 0.130 | 287 | 8 |
| TM12A | 276 | 0.129 | 291 | 8 |
| TM11A | 284 | 0.148 | 303 | 7 |
| Boedickker |  |  |  |  |
| EP64A | 325 | 0.216 | 268 | 4 |
| Un-named Crater EP69A | 293 | 0.242 | 276 | 6 |
| Isidis |  |  |  |  |
| IP84A | 488 | 0.227 | 393 | 15 |
| IP96B | 507 | 0.226 | 379 | 18 |
| Merid Crater |  |  |  |  |
| TM15A | 321 | 0.133 | 311 | 8 |
| TM16A | 316 | 0.132 | 309 | 7 |
| Merid High |  |  |  |  |
| TM13A | 325 | 0.180 | 289 | 12 |
| TM24B | 340 | 0.183 | 291 | 12 |
| NE VM Outflo VM37A | 507 | 0.144 | 331 | 20 |
| Central VM VM44A | 638 | 0.130 | 311 | 18 |
| Ganges VM42A | 436 | 0.137 | 284 | 13 |

### COARSE INTERPRETATION OF NADIR LANDING SITES

Hematite Sites

Moderate Thermal Inertia and Fine Component Thermal Inertia, Very Low Albedo, Few Rocks

Completely Unlike the 3 Landing Sites, Probably Little Dust

Boedickker Crater, EP64A and Unnamed Crater, EP69A

Thermal Inertia & Albedo Sim to VL and MPF Sites, but few rocks

Probably Like 3 Landing Sites – Moderately Dusty, but few rocks

Isidis Sites

High Thermal Inertia and High Fine Component Thermal Inertia, Moderate Albedo, High Rock Abundance, [High Red/Blue Ratio, N]

Rocky Sites with Possibly Weathered Crusty Surface

Meridiani Crater, TM15A, TM16A

Moderate Thermal Inertia, Low Albedo, Average Rock Abundance

Sites probably have average rock abundance with little dust

Meridiani Highlands, TM13A, TM24B

Moderate Thermal Inertia and Low Albedo, Moderate rocks

Sites with moderate rock abundance and little dust

Valles Marineris Sites, NE VM Outflow, VM37A; Central VM, VM44A; Ganges, VM42A

High Thermal Inertia and fine component thermal inertia, Low Albedo and high rock abundance

Rocky sites with well developed duricrust and little dust

Elysium Flow Sites

Moderate Thermal Inertia, High Albedo, Moderate Rocks

Moderately Rocky and Dusty

Ares Vallis Tributary

Mod/High Thermal Inertia, High Albedo, Low/Mod Rocks

Low/Moderate Rocks with Moderate Dust

Sinus Meridiani

High Thermal Inertia, Mod Albedo, Rocky

Rocky with Moderate Dust

Highlands

Moderate Thermal Inertia, High Albedo, Moderate Rocks

Moderately Rocky and Dusty

THERMAL INERTIA VERSUS ALBEDO

THERMAL INERTIA VERSUS ALBEDO

PLOT OF THERMOPHYSICAL PROPERTIES

Plot from Golombek et al. [2001] LPSC XXXII, Abstract #1115.

Table of Slope and Relief Properties of Potential MER Landing Sites

MOLA Data [ROTO Sites followed by Nadir Sites]

| Site | Pulse Width (m) | RMS Slope (deg.) | Median Slope (deg.) | IQS (m) |
| --- | --- | --- | --- | --- |
| ROTO |  |  |  |  |
| Gale Crater | 5 | 6 | 3 | 100 |
| Gusev Crater | 6* | 3 | 1 | 75 |
| Hematite Terra Meridiani | 2 | 1 | 0.5 | 25 |
| Isidis Planitia | 4 | 2 | 1 | 50 |
| Melas Chasma | 5 | 6 | 4 | 100 |
| Eos Chasma, VM Out | 4 | 8 | 2 | 125 |
| Nadir |  |  |  |  |
| Boedickker Crater | 4* | 5 | 2 | 50 |
| Candor SW | 12 | 8 | 4 | 100 |
| Candor NE | 8 | 10 | 8 | 250 |
| Central Valles Marineris | 4 | 12 | 5 | 200 |
| EP69A Unnamed Crater | 6 | 6 | 2 | 75 |
| Ganges Chasma | 8 | 10 | 5 | 175 |
| Meridiani Crater | 4 | 3 | 1 | 50 |
| Meridiani Highlands | 4 | 3 | 1 | 50 |
| NE VM Out | 4 | 6 | 3 | 100 |
| Other |  |  |  |  |
| Pathfinder |  | 3 | 1 | 50 |
| Viking 1 |  | 1 | 1 | 25 |

Data From

Aharonson, O., M.T. Zuber and D.H. Rothman, Statistics of Mars' topography from MOLA: Slopes, correlations and physical models, J. Geophys.Res., in press, 2001.

SLOPE AND PULSE SPREAD

[Site Ellipses, Average]

# Site                      		1.2km Slope				Pulse Spread ______________

# Mean	StdDev.	MaxValue	MinValue	   	Mean	StdDev.	MaxValue	MinValue

# Hematite9A	0.25		0.31		4.22		0.002		0.76		0.25		2.73		0.02

# Hematite19B	0.30		0.37		2.59		0.002		0.76		0.43		6.32		0.02

# Hematite20B	0.21		0.21		2.43		0.007		0.71		0.29		3.64		0.00

# Hematite10A	0.24		0.29		2.53		0.007		0.76		0.30		3.37		0.03

# Hematite21B	0.21		0.29		4.15		0.005		0.64		0.26		4.68		0.10

# Melas53A		1.49		1.74		15.33	0.072		1.66		1.22		9.84		0.00

# MelasB		1.49		1.51		11.86	0.072		1.87		1.50		11.9		0.00

# Isidis85A		0.40		0.70		4.43		0.004		1.22		0.93		15.4		0.01

# Isidis98B		0.53		0.86		8.22		0.005		1.19		0.76		11.01	0.03

# EosChasma	1.01		1.40		11.47	0.016		0.84		0.82		7.60		0.00

# Gale			2.15		2.33		14.92	0.031		1.45		1.37		10.1		0.00

# Gusev		0.60		0.93		6.82		0.015		2.15		0.90		4.69		0.44

VL1			0.29		0.58		9.99		0.003

VL2			0.26		0.18		1.5		0.003

MPF			0.31		0.76		9.25		0.0004

SLOPE AND PULSE SPREAD

Latest Ellipses (Along Track)

| Landing Site | Slope Mean (°) | Slope Std. Dev. (°) | Pulse Width Mean | Pulse Width Std. Dev. |
| --- | --- | --- | --- | --- |
| ROTOs |  |  |  |  |
| Elysium Flow |  |  |  |  |
| EP49B | 1.28 | 3.74 | 1.24 | 0.45 |
| Eos |  |  |  |  |
| VM41A | 5.13 | 6.91 | 1.09 | 0.98 |
| Gale |  |  |  |  |
| EP82A | 6.05 | 6.86 | 1.15 | 0.76 |
| Gusev |  |  |  |  |
| EP55A | 1.36 | 1.75 | 2.16 | 0.98 |
| Hematite |  |  |  |  |
| TM9A | 0.57 | 1.78 | 0.72 | 0.18 |
| TM10A | 0.61 | 0.79 | 0.84 | 0.33 |
| TM19B | 0.38 | 0.47 | 0.72 | 0.21 |
| TM20B | 0.5 | 0.69 | 0.78 | 0.24 |
| Isidis |  |  |  |  |
| IP85A | 1.03 | 3.1 | 1.43 | 0.99 |
| IP98B | 3.74 | 6.64 | 1.09 | 0.78 |
| Melas |  |  |  |  |
| VM53A | 6.52 | 8.48 | 1.13 | 0.88 |
| B Site | 6.62 | 8.76 | 1.16 | 0.92 |

SLOPE AND PULSE SPREAD

Latest Ellipses (Along Track)

| Nadirs |  |  |  |  |
| --- | --- | --- | --- | --- |
| Boedickker Crater |  |  |  |  |
| EP64A | 2.7 | 4.67 | too far S for data | too far S for data |
| Central Vallis Mar. |  |  |  |  |
| VM44A | 11.01 | 12.53 | 1.89 | 1.39 |
| EP69A Crater |  |  |  |  |
| EP69A | 2.37 | 2.72 | 2.16 | 0.86 |
| Hematite |  |  |  |  |
| TM11A | 2.6 | 4.48 | 1.23 | 1.02 |
| TM12A | 1.39 | 1.86 | 0.78 | 0.61 |
| TM21B | 0.62 | 0.63 | 0.6 | 0.34 |
| TM22B | 1.64 | 3.40 | 0.75 | 0.35 |
| TM23B | 0.84 | 0.90 | 0.7 | 0.32 |
| Isidis Planitia |  |  |  |  |
| IP84A | 1.38 | 4.16 | 1.16 | 0.6 |
| IP96B | 0.52 | 1.16 | 1.17 | 0.36 |
| Meridiani Crater |  |  |  |  |
| TM15A | 1.30 | 2.71 | 0.77 | 0.43 |
| TM16A | 1.99 | 4.13 | 0.95 | 0.68 |
| Meridiani Highlands |  |  |  |  |
| TM13A | 1.26 | 2.16 | 0.95 | 0.46 |
| TM24B | 1.38 | 2.09 | 0.94 | 0.33 |
| NE Vallis Mar. Outflow |  |  |  |  |
| VM37A | 4.27 | 6.86 | 1.7 | 1.02 |
| New Highlands |  |  |  |  |
| Ares Vallis Trib. | 1.88 | 1.79 | 1.37 | 0.7 |
| Sinus Meridiani Highlands | 0.59 | 0.52 | 0.96 | 0.29 |
| Highlands | 1.79 | 1.94 | 1.94 | 0.97 |

POSSIBLE ELLIPSE SHIFTS

HEMATITE – Slight Shifts Possible, More Ellipse in Hematite

TM21B South and East to avoid >-1.3 km contour & Secondary Craters

TM10A to NE

EOS CHASMA –

High Slopes at Ends, Shift to NE or SW, 0.6 km in 12 km, 2.9°

GUSEV – Shift West avoid 0.4 km in 6 km, 3.8°

Shift South to Get Closer to Channel

GALE – Cannot Fit, Over 1 km Relief at ends of Ellipse

Fails 2° Over 1 km Slope Criterion

MELAS - Barely Fits, Few km at Ends that Exceed 2° Slope Criterion

ISIDIS - Could Move NE to Lower I, [5N, 272W]

NE VM OUTFLOW - Does Not Fit, Steep Slopes E, SW Appears Rough

MERIDIANI HIGHLANDS - Could Move W to Avoid Scarp

MERIDIANI CRATER, SINUS MERID. HIGHLANDS, HIGHLANDS - OK

EP69A – Does Not Fit, Ellipse is 20 km too Long

BOEDICKKER - Does Not Fit, Ellipse is 35 km too Long

ARES VALLIS TRIBUTARY – Could Move S

ELYSIUM FLOW – Could Move

SITES WITH PROBLEMS AND/OR CONCERNS

PROBLEMS

GALE, BOEDICKKER, EP69A – Ellipse Does Not Fit, Dusty

NE VM OUTFLOW – Ellipse Does Not Fit, West Half Rough

Central Valles Marineris – Ellipse Does Not Fit

CONCERNS

GUSEV – BiModal and High Pulse Spread, Dusty

MELAS – Slopes over 1.2 km Length are High

ISIDIS, EOS, Central & NE VM – Very High Thermal Inertia, Rocky >15%

IP85A, IP84A Just High Thermal Inertia, Could Move N to Lower I

ELYSIUM FLOW - Dusty

SITES WITHOUT PROBLEMS AND/OR CONCERNS

HEMATITE

MERIDIANI CRATER AND HIGHLANDS